## Slide 1: Trans-FW: Short Circuiting Page Table Walk in Multi-GPU Systems via Remote Forwarding
Bingyao Li1, Jieming Yin2, Anup Holey3, Youtao Zhang1, Jun Yang1, Xulong Tang1
1University of Pittsburgh, 2Lehigh University, 3NVIDIA
HPCA 2023 – section 3B

## Slide 2
Ever-growing application complexity and input dataset sizes
Why Multi-GPU Systems?
Single GPU is insufficient to satisfy performance demands
Multi-GPU systems enable further scaling
Multi-GPU is here ! (NVIDIA DGX, Intel Xe)

## Slide 3
Multi-GPU Scalability
Chart: 
| 1-GPU | 2-GPUs | 4-GPUs
Series 1 | 1 | 1.85 | 2.35
x
NUMA data access
Data transfer
Address translation
……
2.4x
1.8x
x
x
x
x
x
[1] https://developer.nvidia.com/blog/easy-multi-gpu-deep-learning-digits-2/

## Slide 4
Multi-GPU Scalability
Chart: 
| 1-GPU | 2-GPUs | 4-GPUs
Series 1 | 1 | 1.85 | 2.35
x
NUMA data access
Data transfer
Address translation
1.8x
2.4x
x
x
x
x
x
[1] https://developer.nvidia.com/blog/easy-multi-gpu-deep-learning-digits-2/
Before data access
On the critical path

## Slide 5
Address Translation Hampers Scalability
Address translation process
latency penalties :
UVM driver (Software)
Local page fault
GPU0
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
GPU1
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
3
1
Waiting in the GMMU PW-queue
Memory access in the GMMU PT-walk
Handling local page fault
2
3
+
+
Driver handled local page fault
1
2
Host MMU handled local page fault
Host MMU
TLB
PW-cache
CPU
PW-queue
PT-walk
Host MMU approach

## Slide 6
Performance Overhead for Address Translation
GPU
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
Chart: Time percentage
| MT | MM | PR | KM | C2D | SC
GMMU PW-queue | 29 | 0 | 0 | 33 | 353 | 1
GMMU PW-cache miss | 261 | 220 | 225 | 246 | 221 | 196
Interconnect+Replay | 411 | 370 | 375 | 396 | 371 | 346
Host MMU PW-queue | 609 | 647 | 610 | 607 | 560 | 637
Host MMU PW-cache miss | 272 | 195 | 178 | 200 | 205 | 188
Page migration | 1290 | 1290 | 1090 | 1290 | 1290 | 990
Local page fault latency
Handling local page faults causes significant overhead Accounts for 86.1% of the L2 TLB miss latency
Address translation related – 50%
Host MMU PW-queue – 20%
Why such high local page faults
handling overheads?

## Slide 7
Page Sharing Characterization
Chart: Page sharing of all accesses
| MT | MM | PR | KM | C2D | SC
One GPU | 147456 | 0 | 4 | 131072 | 585374 | 3
Shared by 2 | 0 | 0 | 0 | 0 | 482035 | 0
Shared by 3 | 0 | 0 | 0 | 0 | 7127 | 0
Shared by 4 | 147648 | 13255883 | 30066404 | 1116605 | 200957 | 3052908
Chart: PW-cache hit rate
| MT | MM | PR | KM | C2D | SC
L5 | 0.0084264 | 1.8579e-05 | 0 | 0.0011387 | 0.0008099 | 0.0086533
L4 | 0.82216 | 0.25424 | 0.17632 | 0.20805 | 0.26472 | 0.33919
L3 | 0.082166 | 0.2565 | 0.27793 | 0.29273 | 0.35027 | 0.20302
L2 | 0.057246 | 0.48347 | 0.53635 | 0.45283 | 0.3386 | 0.40349
Significant pages shared by multiple GPUs
Page migration -> local page faults
Address translation sharing
Observation:
Local PW-cache misses and page faults can
be resolved by other GPUs
Observation:

## Slide 8
Insights
The current address translation process is not efficient due to substantial local page faults.
Significant local page faults make the GMMU page table walk unnecessary.
It is beneficial to mitigate host MMU contention by employing the remote GPU to serve the translation requests.

## Slide 9
Trans-FW (Translation Forwarding)
Request
GPU L2 TLB miss
Remote
GMMU1
Host MMU
GMMU0
Short circuiting in GMMU
Short circuiting in host MMU
Pending
Request Table
Forwarding Table

## Slide 10
Short Circuiting in GMMU
GPU
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
Short circuit the translation in GMMUs by eagerly sending the request to the host MMU upon an L2 TLB miss.
Allow the potential local page faults to be served early by the host MMU.
An excessive number of requests being sent to the host MMU.
 | invalid
unnecessary

## Slide 11
Short Circuiting in GMMU
GPU
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
PRT
tracks the translations of all pages that reside in the GPU’s local memory.
Pending Request Table (PRT) :
h1(key)
PRT
key
Cuckoo hash
h2(key)
bucket
compare
True/False
……
finger
print
VPN | offset
finger print |  |  | 
…… |  |  | 
Employ a Cuckoo filter
If hits PRT, performs local PT-walk.
VPN forms fingerprint
If misses PRT, bypass GMMU, early forwarded to the host MMU without a GMMU PT-walk.

## Slide 12
Short Circuiting in Host MMU
GPU0
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
PRT
GPU1
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
PRT
Short circuit the translation in host MMU by sending translation requests to remote GPUs.
Avoid the contention and potential overheads in host MMU.
The location of valid page can only be obtained after host MMU page table walk.

## Slide 13
Short Circuiting in Host MMU
GPU0
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
PRT
GPU1
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
PRT
Forwarding Table
tracks which GPU has the valid page.
Forwarding Table (FT) :
Employ the same Cuckoo filter
VPN + GPUid forms fingerprint
Accessing remote page tables may take longer than accessing the host page table due to network congestion and remote PT-walk contention.
When to forward ?

## Slide 14
Short Circuiting in Host MMU
GPU0
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
PRT
GPU1
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
PRT
Forwarding Table
When to forward :

## Slide 15
Short Circuiting in Host MMU
GPU0
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
PRT
GPU1
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
PRT
Forwarding Table
When to forward :
If the number of queued requests less than forwarding threshold, only rely on the host MMU to perform PT-walk.

## Slide 16
Short Circuiting in Host MMU
GPU0
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
PRT
GPU1
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
PRT
Forwarding Table
When to forward :
If the number of queued requests less than forwarding threshold, only rely on the host MMU to perform PT-walk.
If exceeds forwarding threshold, also forwarded to a remote GPU according to the FT.

## Slide 17
Short Circuiting in Host MMU
GPU0
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
Host MMU
TLB
PW-queue
CPU
PW-cache
PT-walk
PRT
GPU1
L2 TLB
GMMU
PW-cache
PT-walk
PW-queue
Compute Unit
Compute Unit
Device memory
Page
table
PRT
Forwarding Table
When to forward :
If the number of queued requests less than forwarding threshold, only rely on the host MMU to perform PT-walk.
If exceeds forwarding threshold, also forwarded to a remote GPU according to the FT.
If the remote lookup succeeds but the request still waits in the host PW-queue, the request is removed from the PW-queue.
succeed

## Slide 18
Methodology
Simulator: MGPUSim [ISCA 19’]
Workloads: 10 applications from Hetero-Mark, AMDAPPSDK , SHOC, and DNN Mark benchmark suites.
Hardware setup:
 | Configuration
Host MMU TLB | 2048 entries, 64 way, GPU shared
Page table walk | Host MMU 16 shared page table walker, GMMU 8 shared page table walker, 100-cycle latency per level
Page table cache | 128 entries shared across page table walker
CPU-GPU interconnection | 150-cycle latency

## Slide 19
Evaluation
Chart: Normalized performance
| MT | MM | PR | ST | KM | Conv2d | SC | Im2col | AES | FIR | Ave.
Trans-FW | 2.3837 | 1.8464 | 1.7666 | 1.5199 | 1.7096 | 1.3702 | 1.5628 | 1.2237 | 1.0009 | 1.0004 | 1.5384
Trans-FW achieves an average of 53.8% performance improvement.

## Slide 20
Evaluation
Chart: Reduced percentage
| MT | MM | PR | ST | KM | Conv2d | SC | Im2col | AES | FIR
PW-cache miss | 0.046154 | 0.029091 | 0.11893 | 0.01049 | 0.046393 | 0.015326 | 0.029899 | 0.00020408 | 0.0073529 | 0.0061162
Local PW-queue | 0.95467 | 0.96552 | 0.95676 | 0.98599 | 0.9697 | 1 | 1 | 1 | 0.87241 | 0.92881
Host MMU PW-queue | 0.85386 | 0.86635 | 0.85625 | 0.99062 | 0.88303 | 0.95429 | 0.97129 | 0.99176 | 0.31429 | 0.25714
Page fault | 0.42733 | 0.49349 | 0.51932 | 0.57884 | 0.43529 | 0.65575 | 0.55489 | 0.59579 | 0.008765 | 0.067427
The reduced percentage of each latency component.
40%

## Slide 21
More Results in the Paper
Sensitivity to forwarding threshold, number of GPUs, PT-walk threads, host-MMU configuration …
Sensitivity to remote access latency
Compared with page replication, remote mapping, large page
Compared with state-of-the-art PW-cache prefetching, TLB optimization

## Slide 22
Problem: Address translation overheads in multi-GPU systems under unified virtual memory.
Key idea: address translation sharing and forwarding
Trans-FW:
Short circuit in GMMU reduces unnecessary page table walks
Short circuit in host MMU mitigates contention in host MMU
PRT & FT with minimal hardware overhead
Improves performance by 53.8% on average.
Three latency penalties in address translation process
Summary

## Slide 23: Trans-FW: Short Circuiting Page Table Walk in Multi-GPU Systems via Remote Forwarding
Bingyao Li1, Jieming Yin2, Anup Holey3, Youtao Zhang1, Jun Yang1, Xulong Tang1
1University of Pittsburgh, 2Lehigh University, 3NVIDIA
Thanks! Q&A
Email: bil35@pitt.edu

## Slide 24
Backup slides

## Slide 25
Driver Handled VS. Host MMU Handled Page Fault
Chart: Number of GPUs
| 4 | 8 | 16 | 24 | 32
Host MMU | 1 | 2.1559 | 3.4346 | 4.2302 | 4.7817
Driver | 1.28 | 2.7135 | 5.5502 | 6.7563 | 9.4286
~ 4.5x
x
x
x
x
x
Host MMU approach
Address translation overheads: driver 4.5x higher than host MMU
Increasing gap between driver approach and host MMU approach

## Slide 26
Evaluation
Percentage of replicated PT-walk to all host MMU PT-walk.
Chart: Replicated PT-Walk
| MT | MM | PR | ST | KM | Conv2d | SC | Im2col | AES | FIR | Ave.
L5 | 0.33456 | 0.39588 | 0.38526 | 0.14605 | 0.3096 | 0.2147 | 0.28049 | 0.1872 | 0.00097774 | 0.00052231 | 0.22552
65% of those replicated requests (i.e., 22.6%) in host MMU are eliminated.
Short-circuiting the local GMMU reduces 49.6% of the total GMMU PT-walk memory accesses.